## Slide 1
Robotic 595R
TILT SENSOR INTEGRATION
Mani Saeidi, Matt Gordon
OFF-ROAD APPLICATION

## Slide 2
The Mission
Features:
  Tilt Sensors
  Warning LEDS.
  Alternative Routes.

## Slide 3
Off-road Background
  Used in 4x4 vehicles for many years for off-road driving.
  Simple bubble level mounted on the dashboard, providing a basic indication of the vehicle's inclination.

## Slide 4
Essential Components
MSP432 on TI Robotics Kit
Tilt Sensor
Sensitivity Pots
Notes: This utility drone, will illuminate trails and points of interest using a remote controller. Video transmission may be considered. The drone shall avoid both stationary and moving obstacles with it's proprietary hardware code. This technology can be used for emergency, military, or civilian use.

## Slide 5
Plans
  Original Plan: GPIO with Interrupts
  Change in Plan: GPIO with Polling
Notes: Using polling where we wait for the device to do a status check instead of an interrupt sending a signal and activating the NVIC whenever there is a flicker.
Simpler mechanism than interrupts to implement and we didn't want constant interrupts if there was flickering between which sensor was being activated at the time due to calibration issues
Future Development: Multiple Cores: Have multiple cores for polling if additional sensors onboard Create a counter or timer for the flickering Automatic Terrain Tracking (Notices if road is off pitch for turns)
[12:35 AM]pikA+:
i dont get it

## Slide 6
Program Implementation
GPIO Pins Utilized on Robot:
P4.0, P4.2, P4.4 & P4.5
P4.0 = 0x01
P4.2 = 0x04
P4.4 = 0x10
P4.5 = 0x20
= 0x35
+__________________

## Slide 7
Program Implementation
Notes: Different operations for which pins were active low

## Slide 8
Demonstration
Video Demo LINK: https://youtube.com/shorts/D-K7hyaTdIc

## Slide 9
Issues We Ran Into
  LEDs displayed the opposite of the expected behavior.
  Flickering of sensor due to calibration issues.
Notes: ssues we ran into:
LEDS of the tilt were on when status of pin was off Flickering of the LED sensor - fixed with a delay although
it wouldve been better to use a debouncer-like system

## Slide 10
Future Development
  Multiple Cores
  Systick Counter to Fix Flickering
  Automatic Terrain Tracking
  AI Crawl Control
Notes: Multiple cores since multiple sensors on future vehicles to handle polling easily instead of waiting for each sensor one by one
Counter can fix flickering so that the operation is only performed if the sensor is active for a certain amount of time

## Slide 11
Sources

## Slide 12
Unlike these presentations,
our inclinometer will keep you level-headed.
Mani Saeidi
Matthew Gordon
MATTI GAEIDI
Conquer Terrain with Ease,
Anywhere That You Please!